EDDSFIELD AIRFIELD

ELEVATION    LOCATION				GAM 112.80 023 52.7

525ft 		     7nm N of Driffield E Yorkshire 	OTR 113.90 337 27.8

27.8

l7mb		     N5406.42 W00027.26

Eddsfield Radio 134.00*    APP/LARS 119.12 (Humberside)

*Not normally manned, make blind calls

RWY  SURFACE      TORA 	LDA	  CIRCUIT	  LIGHTING

09 	     Grass 	         700 	         775 	       LH	       Nil

- Grass 	         775 	         700 	       RH	       Nil

All circuits to the North of the airfield.

Updated information and live airfield weather at www.eastyorkshire.co.uk/eddsfield.

Operator.

Mr Edd Peacock, Eddsfield Airfield, Langtoft, Driffield. East Yorkshire Y025 3BJ

Tel: 01377 267368	Tel: 07970 482539 (Mobile)    email: eddsfield@eastyorkshire.co.uk

Visiting ACFT welcome, PPR and at pilot's own risk. Well equipped caravan clubhouse.      Rwys well prepared with white designators.	   Avgas 100LL available. Hangerage available.

Warnings.

There are 2 telecommunication masts close to the S of Rwy 27 APP. One on very short final is 120ft. The second approx 900 metres out is 150ft agl. Mature trees on short final for Rwy27 up to 80ft agl may cause rotor or roll-over, Rwy27 landing Thr is displaced to take them into account.

Noise:

Do not over fly crematorium which is a new building S of Rwy27 APP on short final. Do not over fly Octon/Thwing village.